## Slide 1
Properties of Crude Oil Responsible for Pipeline Accidents
Date: January 29, 2023
Created By: Cameron MacKinnon

## Slide 2
Table of Contents
Problem Statement
Scope
  Pipeline Accidents
  Pipeline Materials
Approach
  Physical and Chemical Properties of Crude Oil
  Hypothesis
Datasets
Analysis
Results
Conclusion / Future Investigation
Regulations & Implications
References
Appendix

## Slide 3
Problem Statement
What qualities of crude oil lead to pipeline accidents and what are the related regulations?
Part A
Part B – Regulations & Implications
What physical or chemical properties of crude oil could be responsible for pipeline accidents?
- What regulations on those properties would you recommend?
- Have we gotten better at regulating those properties over time?
- What implications on the oil market would these regulations have?
- How can success of these regulations be quantified in the short term and long term?

## Slide 4
Part A – Physical or Chemical Properties of Crude Oil that could be Responsible for Pipeline Accidents

## Slide 5
Crude Oil
Physical Properties
CLASS A: LIGHT, VOLATILE OILS [2]
CLASS B: NON-STICKY OILS
Highly fluid
Often clear
Spread rapidly on solid or water surfaces
Have a strong odor
High evaporation rate
Usually flammable
Waxy or oily
Less toxic
Penetrate porous substances
Evaporation of volatiles leads to Class C or D residue
CLASS C: HEAVY, STICKY OILS
Viscous
Sticky or tarry
Brown or black
CLASS D: NON-FLUID OILS
Relatively non-toxic
Do not penetrate porous substances
Black or dark brown
To determine what underlying properties of crude oil could be contributing to pipeline accidents, we need to first understand the composition of crude oil. This includes its chemical composition, its physical properties, and any additional qualities that could be related to pipeline incidents.
The weight of crude oils is measured on an arbitrary scale based on their relative gravity/density to water, where water has 10 API gravity. Heavy crudes have an API of 22 or below, lighter crudes generally exceed 38 API. [3]
Chemical Properties
Crude Oil is also known for containing varying concentrations of sulfur.
SOUR: >=0.5% sulfur content
General
Crude oils are primarily composed of hydrocarbon gases and liquids. A sample breakdown of Bakken crude oil, considered a light crude oil, is given in Appendix A [1]. [anything else here cam???!!!] talk about chemical physical ….
SWEET: <0.5% sulfur content

## Slide 6
Pipeline Accidents
The PHMSA lists 10 unique causes for pipeline failures along with notable characteristics and what percentage they make up of total pipeline incidents [5]. Given these failure types, we want to determine which could be potentially relevant to our analysis so that we can filter our data accordingly.
Pipeline Failure Cause | Description | 1998-2017 Percentage Pipeline Accidents | Weight-relevant? | Sulfur-relevant?
External Corrosion | Due to environmental conditions on the outside of the pipe | 8 % | No | No
Internal Corrosion | Contaminants naturally contained within the transported commodity, such as hydrogen sulfide, carbon dioxide, or other chemicals | 12 % | No | Yes
Stress Corrosion Cracking | Environmentally-assisted cracking that reduces the pressure-carrying capability of the pipe | 1 % | Maybe | Maybe
Selective Seam Corrosion | Localized corrosion along specific welding points. Generally, has been fixed since 1970 due to upgrade materials. | 1 % | No | No
Excavation Damage | Excavator damaging exterior of pipeline | 15 % | No | No
Natural Force Damage | Naturally occurring events, such as earth movement or heavy rains. | 9 % | No | No
Other Outside Force Damage | Vehicle or equipment contact; vandalism; damage caused by accidents, etc. | <1 | No | No
Material/Weld Failure | Impurities remaining in the molten steel upon manufacturing. | Not Provided | Maybe | Maybe
Equipment Failure | Pipeline component other than the pipe. E.g., pumps and compressors, meters and metering equipment, valves | Not Provided | Yes | Maybe
Incorrect Operation | Direct or indirect cause of a pipeline failure; e.g., wrong valve open, overfilling a tank, over-pressuring a piece of equipment | Not Provided | No | No
Key Takeaways
PHYSICAL PROPERTIES
Focus on accidents in which the weight of the substance could have exacerbated stress corrosion, or material/equipment failure.
CHEMICAL PROPERTIES
Focus on incidents in which internal corrosion occurred, or material failures where the substance could have deteriorated the performance of the equipment/system.

## Slide 7
Dataset Collection
We need to source data that contains information on pipeline incidents. The ideal dataset will contain detailed information on the substances that are being transported and the cause of the accident. Additional information about pipeline specifications could be valuable.
The Canada Energy Regulator (CER) (formally the National Energy Board) regulates pipelines that cross inter-provincial or international boundaries; pipelines that are intra-provincial are regulated by each individual province [6]. The Onshore Pipeline Regulations (OPR) were created by the CER to ensure companies are meeting pipeline safety requirements.
Label | Dataset Name | Description | Date Range | # Records | Crude Oil Types | Weight-specific info? | Sulfur-specific info? | Accident-specific info
A | Pipeline-incidents-comprehensive-data.csv | Pipeline incidents as defined by OPR and Processing Plant regulations | 2008 to Present | 1856 | Crude Oil, Crude Oil (Heavy, Light, Sour, and Sweet) | No | No – grouped together | What happened: damage, deterioration, construction, etc.; Incident type: fire, release of substance, etc.
B | PODSdb_MDOTW_VW_OCCURRENCE_PUBLIC.csv | Incidents at CER-regulated pipelines and facilities as defined by OPR | 2008 to current | 3265 | Crude Oil, Crude Oil-Sour | No | Sour vs. not sour | Classification of Occurrence (encoded); occurrence summary
C | Accident_hazardous_liquid_pre1986.txt | Incidents within Hazardous Liquid and Carbon Dioxide Pipelines from 1968 to 1985 | 1968 to 1985 | 4734 | Crude Oil | No | No | PRIMARY_CAUSE: corrosion, equipment, defective pipe, etc.
D | Accident_hazardous_liquid_1986_jan2002.txt | ^ [1986:2002] | 1986 to 2002 | 3095 | Crude Oil | No | No | CAUS: corrosion, failed pipe, malfunction, etc. ; CAUSO: breakdown of CAUS; NARRATIVE
E | Accident_hazardous_liquid_jan2002_dec2009 | ^ [2002:2009] | 2002 to 2009 | 3031 | Crude Oil, Crude Oil Heavy, Crude Oil Sour, Crude Oil / Location, and more | Not explicitly; can be roughly extrapolated | Not explicitly; can be roughly extrapolated | Small spills: GEN_CAUSE (equipment, corrosion, etc.) Big spills: CAUSE (more detailed than small spills); NARRATIVE
F | Accident_hazardous_liquid_jan2010_present | ^ [2010:2023] | 2010 to 2023 | 5248 | Crude Oil | No | No | CAUSE: corrosion, equipment, manual error, etc. CAUSE_DETAILS: more detailed than above; NARRATIVE
G | Accident_gravity_reporting_regulated_jul2020_present.txt | Transportation incidents of hazardous liquids flowing through gravity pipelines. | 2021 to 2023 | 297 | Crude Oil (Nothing else) | No | No | CAUSE: corrosion, equipment, manual error, etc. CAUSE_DETAILS: more detailed than above; NARRATIVE
The Pipeline and Hazardous Materials Safety Administration (PHMSA) is responsible for regulating and ensuring the safe and secure movement of hazardous materials within the United States [7].
Canadian Datasets*
American Datasets
*Omitting pipeline transportation occurrence data from Jan 1979 to 1990 as the TSB does not warrant the quality, accuracy, reliability or completeness of its data [8]

## Slide 8
Approach
Before diving into a dataset, we need to ensure that we’re taking a logical approach to the problem that encompasses the possible scenarios / outcomes.
Approach #1 – Crude Oil vs. NOT Crude Oil
One way to determine whether the physical or chemical properties of crude oil influence pipeline accidents is to look at accidents that involved crude oil versus accidents that involved transporting other substances (e.g., natural gas). If there is a discernable difference between accidents for different substance types, we may be able to infer that there are inherent properties of crude oil (that don’t exist / are less prominent in other substances) that are contributing to these incidents.
Approach #2 – Inherent Properties of Crude Oil
The second, and perhaps more direct approach to the problem, is to evaluate crude-oil specific incidents to see if its variations in composition (heavy vs. light, sour vs. sweet) are a direct contributor to pipeline accidents.
Considerations for Dataset Selection
Given that we have both Canadian and American datasets, it would be ideal to analyze at least one of each because:
  1) The data that is required by the governing bodies may vary and therefore result in different attributes / information provided about the incident
  2) Canada and the USA have varying geographies, and this may influence substance properties (e.g., difference in temperature could affect corrosion rates)
  3) Because Canada and the USA have different governing bodies for their pipelines, the pipeline-specific specifications (e.g., what materials meet code to build pipelines) may vary, which could contribute to pipeline incidents based on the substance being transported
Additionally, it seems logical to select data that is as recent as possible and to select datasets with the highest number of records (assuming they are of decent quality).
DATASET COLLECTION
Given the desired approaches and considerations for dataset selection, dataset A (Canada) will be selected for Approach #1 and dataset E (USA) for Approach #2.
Dataset E had to be used for Approach #2 given that it is the only dataset that contains property-specific information about the crude oil being transported*. That left the two Canadian datasets for Approach #1; dataset A was selected because dataset B contained information about incidents at pipeline facilities / processing plants which is outside of the scope of this analysis.
*Dataset B contains crude oil vs. crude oil-sour, however, only two of the hundreds of crude oil records are crude oil-sour.

## Slide 9
Analysis – Approach #1
The key steps taken in the analysis of Approach #1 are summarized below. The corresponding script for this analysis is in the “dataset_A.ipynb” file, which falls under the “src” folder. The script itself includes further explanation of the decision-making process.
Step | Description
1. Data Ingestion | 1.1 Load in dataset A given its relative location to the root directory.
2. Data Cleaning | 2.1 Clean the dataframe so that it can be used in analysis. Use information from the dataset’s corresponding data dictionary
 | 2.1 Identify columns from data dictionary that could be relevant to 1) the inherent properties of the substance being carried, 2) pipeline specifications, or 3) the cause of the incident.
 | 2.2 Optimize the substance carried column using the released substance type column. Want to perform this task before dropping attributes that don’t meet a specific threshold. Additionally, map any substance that does not equal crude oil to 0, and any crude oil substance to 1.
 | 2.3 Drop any attributes (columns) that are less than 50% populated.
 | 2.4 Clean numeric columns
 | 2.5 Map categorical columns to binary/numeric.
 | 2.6 Map descriptive columns (e.g., “what happened category”) to binary columns, i.e., one-hot encode.
3. Data Exploration | 3.1 Generate a profiling report of the dataframe to generate a heatmap, identify highly correlated pairs, or display errors / inconsistencies in the dataset (e.g., duplicate rows).
 | 3.2 Output descriptive statistics (count, mean, etc.) of numeric columns to identify additional trends.
4. ML Models | 4.1 Preprocess dataframe for ml models by running a correlation matrix and dropping one of the columns found in each high-correlated pair.
 | 4.2 Run a logistic regression model on the data to identify if substance type (crude oil vs. not crude oil) can be predicted by the other attributes.
 | 4.3 Random forest.
 | 4.4 Decision tree.
 | 4.5 Support Vector Machine (SVM).

## Slide 10
Analysis – Approach #2
Similar to the previous slide, the key steps taken in the analysis of Approach #2 are summarized below. The corresponding script for this analysis is in the “dataset_E.ipynb” file. Once again, the script itself includes further explanation of the decision-making process.
Step | Description
1. Data Ingestion | 1.1 Load in dataset E given its relative location to the root directory.
2. Data Cleaning | 2.1 Prioritize the commodity column as their properties (sweet vs. sour, heavy vs light) are the basis of this analysis.
 | 2.2 Map these properties to binary columns using string extrapolation. E.g., “Heavy Louisana Sweet” would mark a 1 in the “heavy” and “sweet” columns. These properties were only given for a tiny portion (~45/1355) of the records.
 | 2.3 Identify and fill in the general cause of the incident using logic from the corresponding data dictionary.
 | 2.4 Clean the remaining columns using a similar process to that for dataset A / Approach #1.
3. Data Exploration | 3.1 Generate a profiling report of the dataframe to generate a heatmap, identify highly correlated pairs, or display errors / inconsistencies in the dataset (e.g., duplicate rows).
4. ML Models | 4.1 Preprocess dataframe for ml models by running a correlation matrix and dropping one of the columns found in each high-correlated pair.
 | 4.2 Run a decision tree model on the data to identify if the specific properties of the crude oil had an affect on the incident type.
 | 4.3 Random forest.
 | 4.4 Logistic regression.
Incomplete | The majority of the steps from 2.3 - onwards were performed and iterated upon in an attempt to salvage the approach. Ultimately, the minimal number of records (~45) with property-specific information on crude oil limited the extent of this analysis.

## Slide 11
Conclusions / Key Takeaways – Approach #1
……
Approach #1 – Crude Oil vs. NOT Crude Oil
- able to predict crude oil vs. not crude oil using latitude and longitude, and pipeline diameter and length
- the success of the above implies that crude oil pipelines are in different locations than their counterparts and even have slightly different pipeline specifications – specifically the diameter and length of their pipelines
- But when I remove these attributes, I am left with mediocre results
Sample of these results from Random Forest after the four above attributes have been removed:
Precision / recall / accuracy
Interpretation:
# good at predicting not crude oil, not good at predicting crude oil
# we could conclude that there are potentially inherent differences in not crude oil vs. crude oil accidents
## and therefore further investigation into their differences is warranted
Future investigation/analysis
## look into specific attributes contributing to NOT crude oil incidents to determine why these attributes are more pronounced than those of crude oil
## look into crude oil/not crude oil vs. NON-incidents to determine what properties of the substances are causing the accidents in the first place
## feature engineering - removing less important attributes based on domain knowledge; aggregating attributes if possible
## expanding dataset by concating other relevant data files

## Slide 12
Conclusions / Key Takeaways – Approach #2
……
Approach #1 – Crude Oil vs. NOT Crude Oil
…

## Slide 13
Regulations & Implications
Looking at … data in 2 steps

## Slide 14
Approach
About crude oil
- made up of hydrocarbons (by weight carbon, some hydrogen)
- Physical properties: can be light, medium, or heavy – API gravity
- Chemical properties: can be sour or sweet depending on sulfur content
Hypothesis
- sour is more corrosive than sweet
- heavier affects how it flows – more pressure and energy required to pump the oil
but light are more flammable
Make sure to use this:
https://www.epa.gov/emergency-response/types-crude-oil
FUTURE INVESTIGATION: material of pipe
Investigating properties of crude oil so that a logical approach can be taken to solve the problem.
Mention that is tartd with dataset A because it focused on pipeline incidents (and not facilities)

## Slide 15
References

## Slide 16
References
TABLE - AFPM - Survey of Crude Oil Characteristics
Types of crude oil – EPA
Measurement of weight (API) for crude oil - https://www.eia.gov/dnav/pet/TblDefs/pet_pnp_crq_tbldef2.asp
Sweet vs. sour - https://www.pipesearch.com/blog/sweet-and-sour-crude-oil/136
Pipeline failure causes (PHMSA) - https://www.phmsa.dot.gov/incident-reporting/accident-investigation-division/pipeline-failure-causes
CER regulation of pipelines - https://natural-resources.canada.ca/our-natural-resources/energy-sources-distribution/fossil-fuels/pipelines/faqs-federally-regulated-petroleum-pipelines-canada/5893#h-4-1
PHMSA - https://www.phmsa.dot.gov/regulations
Jan 1979 TSB datasets - https://www.tsb.gc.ca/eng/stats/pipeline/data-2.html

## Slide 17
Appendix

## Slide 18
Appendix A: ____
Hydrocarbon gas | Concentration in Liquid Volume % | DOT Classification
Methane | <0.01 | Div. 2.1 Gas
Ethane | 0.05 | Div. 2.1 Gas
Propane | 0.80 | Div. 2.1 Gas
Iso-Butane | 0.46 | Div. 2.1 Gas
N- Butane | 2.36 | Div. 2.1 Gas
Total Gas | 3.67 | 
Neopentane | <0.01 | Class3; PG I
Iso-Pentane | 1.33 | Class3; PG I
N-Pentane | 2.36 | Class3; PG II
Hexanes | 4.10 | Class3; PG II
Heptanes Plus | 88.56 | Varies Class 3; PG II to combustible liquid to non-regulated
Benzenes | 0.08 | Class 3; PG II
General
Crude oils are primarily composed of hydrocarbon gases and liquids. A sample breakdown of Bakken crude oil, considered a light crude oil, is given in Appendix A [1]. The DOT classification is a measurement of flammability (2.1 for gases, 3 for liquids).